K32     PANEL CUBICLES

120     PANEL CUBICLES - UNFRAMED

Manufacturer: Formwise Washrooms Ltd, Unit 3 Wendel Point, Park Farm, Wellingborough, Northamptonshire NN8 6BA

T: 01933 405961 F: 01933 405971

Email: sales@formwise-washrooms.co.uk

Web: www.formwise-washrooms.co.uk

Product reference: ‘art mfc’ toilet cubicles

Panels & Doors: 19mm high performance moisture resistant (MR) melamine faced 710kg/m3 chipboard (MFC).

Core material: Not applicable.

Finish: Velour.

Colour: Colour to be confirmed from Formwise Washrooms MFC selection.

Edge treatment: All edges are lipped with matching/contrasting

durable 1mm PVC.

Pilasters: Smooth extruded aluminium.

Core material: Aluminium.

Colour: Powder coated finish to any RAL colour.

Edge treatment: Radiused edges.

Headrails: Extruded aluminium powder coated to match pilasters

Legs: Polished aluminium design, fixed into divisions, adjustable to accommodate varying floor levels.

Ironmongery/ Accessories: Aluminium pivot hinges / Coat hook / Ergonomic DDA compliant slide operated indicator bolt with circular face plate / Integral door buffer and emergency release facility.

Finish/ Colour: Polished aluminium

Dimensions: 2010mm overall height including 160mm floor clearance

Other requirements: Complete with outward opening doors to ambulant and enlarged cubicles where requested. Cubicles with inward opening doors to be set out to maintain 450mm diameter manoeuvring space within the cubicle.