K32     PANEL CUBICLES

120     PANEL CUBICLES - UNFRAMED

Manufacturer: Formwise Washrooms Ltd, Unit 3 Wendel Point, Park Farm, Wellingborough, Northamptonshire NN8 6BA

T: 01933 405961 F: 01933 405971

Email: sales@formwise-washrooms.co.uk

Web: www.formwise-washrooms.co.uk

Product reference: ‘art tall hpl’ toilet cubicles

Doors: 18mm moisture resistant chipboard faced both sides with high pressure laminate (HPL).

Core material: Moisture resistant chipboard (to V313).

Finish: Velour.

Colour: Colour to be confirmed from Formwise Washrooms HPL selection.

Edge treatment: Edges are lipped in 2mm PVC lipping

Panels: 18mm moisture resistant chipboard faced both sides with high pressure laminate (HPL).

Core material: Moisture resistant chipboard (to V313).

Finish: Surf.

Colour: Colour to be confirmed from Formwise Washrooms HPL selection.

Edge treatment: Edges are lipped in 2mm PVC lipping.

Pilasters: Smooth extruded aluminium.

Core material: Aluminium.

Colour: Powder coated finish to any RAL colour.

Edge treatment: Radiused edges.

Headrails: Extruded aluminium powder coated to match pilasters

Ironmongery/ Accessories: Aluminium pivot hinges / Coat hook / Ergonomic DDA compliant slide operated indicator bolt with circular face plate / Integral door buffer and emergency release facility.

Finish/ Colour: Polished aluminium

Dimensions: Up to 2800mm overall height

Other requirements: Complete with outward opening doors to ambulant and enlarged cubicles where requested. Cubicles with inward opening doors to be set out to maintain 450mm diameter manoeuvring space within the cubicle.